## Slide 1: cMoflon: Model-Driven Generation of Embedded C Code for Wireless Sensor Networks
Conference Talk at ECMFA 2017
2017-07-19
Specification
Testbed
cMoflon

## Slide 2: The curse of low abstraction in traditional communication system development
(i) Specification: Graph theory, …
(ii) Simulation:
C, Java, …
(iii) Testbed: C, C++,…
Feedback &
refinement
Implementation
Formalization, proofs,…
Constraints ✓
Model
</>
Level of abstraction
Porting
Limitations ✓
Code
https://www.flocklab.ethz.ch/wiki/chrome/site/wiki_public/observer/outdoor_1.jpg
Notes:   Level of abstraction drops early [Qadir15, Rexford13, Julien13]
  Network protocols are usually analyzed after the fact [Zave12, Zave08]
  Specification-to-implementation step is intransparent [Qadir15, Rexford13, Julien13]
[Quadir15] Qadir, Hasan: "Applying Formal Methods to Networking: Theory, Techniques, and Applications", IEEE Comm. Surveys & Tutorials, 2015
[Rexford15] Rexford, Zave: "Report of the DIMACS working group on abstr. for netw. services, arch., and impl.", ACM Comp. Comm. Review, 2013
[Julien13] Julien, Wehrle: Preface to SESENA'13 workshop on software engineering for sensor network applications (at ICSE'13)
[Zave12] Zave: "Using lightweight modeling to understand chord," SIGCOMM Comput. Commun. 2012
[Zave08] Zave: "Understanding SIP through Model-Checking," LNCS 5310, 2008

## Slide 3: Leverage model-driven engineering principles!
(i) Specification: Graph theory, …
(ii) Simulation:
C, Java, …
(iii) Testbed: C, C++,…
Formalization, proofs,…
Localization
</>
Constraints ✓
Limitations ✓
Model
Code
Feedback &
refinement
Extensible code gen.
Extensible code gen.
Level of abstraction
Notes: [Völter13, Kluge15]
[Völter13] Völter et al.: "Model-Driven Software Development: Technology, Engineering, Management," John Wiley & Sons, 2013
[Kluge15] Kluge et al.: "A Methodology for Designing Dynamic Topology Control Algorithms via Graph Transformation," in ICMT 2015
http://www.voelter.de/data/books/mdsd-en.pdf
(inspired by success stories of model-based approaches to WSN applications programming, e.g., Scatterclipse)

## Slide 4: Contribution
(i) Specification: Story-driven modeling
(ii) Simulation:
Java
(iii) Testbed
eMoflon
Extensible code. gen
+
Previous: Integration with wireless network simulator
(i) Specification: Story-driven modeling
(iii) Testbed: Embedded C
(ii) Simulation
cMoflon
This paper: Code generation for wireless sensor testbed
Extensible code. gen
+
</>
</>

## Slide 5: Wireless Sensor Networks
Transmission range
Wireless node n2 + hop count h1(n2) to n1
Wireless link e34
+ link weight w(e34) (e.g. distance approx. via RSSI)
TelosB sensor node [Polastre05] (48kB ROM, 10kB RAM)
[Polastre05] Polastre et al.: "Telos: enabling ultra-low power wireless research," IPSN 2005
n2 1
n3
1
2
2
2
3
n1
0
n4
2
x
y
Wireless Sensor Network
Notes: Wireless Sensor Network: resource-constrained devices, ad-hoc communication, e.g., for wildlife monitoring, wildfire detection
Topology: graph that represents devices and comm. links
Graph-based model of topologies:
nodes -> devices (with communication range and adjustable transmission power)
edges -> communication links
additional attributes: edge weight = link length, received signal strength indicator (RSSI), …
    Paramount objective: save energy

## Slide 6: Topology Control
High weight means high energy consumption
Inactivate high-weight links
⇒
n2 1
n3
1
2
2
2
3
n1
0
n4
2
Topology Control
x
y
n2 1
n3
2
2
2
2
3
n1
0
n4
3
x
y
Active
Inactive
Hop count increase
Notes: Graph-based model of topologies:
nodes -> devices (with communication range and adjustable transmission power)
edges -> communication links
additional attributes: edge weight = link length, received signal strength indicator (RSSI), …
    Paramount objective: save energy

## Slide 7: Running examples: kTC, l*-kTC, and LMST
Input topology
Output topology
n2 1
n3
1
2
2
2
3
6
n1
0
n4
1
w(eab)
na h1(na)
nb h1(nb)
Legend
n2 1
n3
1
2
2
2
3
6
n1
0
n4
1
kTC[Schweizer16](k=2) Inactivate the weight-maximal link in each triangle
[Schweizer16] Schweizer et al. "a-kTC: Integrating topology control into the stack," LCN'16
[Stein16] Stein et al. "Topology Control in WSNs: What Blocks the Breakthrough?," LCN'16
[Li05] Li et al. "Design and analysis of an MST-based topology control algorithm," IEEE Trans. Comm. 2005
Distance to node n1
Unclassified
Active
Inactive
n2 1
n3
1
2
2
2
3
6
n1
0
n4
1
LMST[Li05] Activate links on local minimum spanning tree
n2 1
n3
1
2
2
2
3
6
n1
0
n4
1
l*-kTC[Stein16] (k=2,a=1.5)
kTC + bound increase of routing path length
Notes: General motivation: These algorithms were implemented in a previous paper within the selected framework
  Establishes comparability
kTC
  Illustrates that cMoflon is suitable to implement weight-based Topology Control algorithms
l*-kTC[Stein16]
  Illustrates how a developer may introduce custom attribute constraints
LMST[Li05]
  Illustrates how a developer may introduce auxiliary classes into the metamodel

## Slide 8: Challenges while building cMoflon
Ensure applicability
  Problem: Unrealistic to build a "one-fits-all" solution
  Approach: Representative algorithms and extensibility
Foster rapid prototyping
  Problem: Porting to testbed incures high manual effort
  Approach: Automation + extension points
Respect resource limitations
  Problem: Resource constraints (e.g., Telos-B: 48kB ROM, 10kB RAM)
  Approach: Use ToCoCo framework for Contiki OS
✓

## Slide 9: Specification
(i) Specification
(ii) Simulation
(iii) Testbed

## Slide 10: Topology Control metamodel
Node
≪abstract≫
TopologyControlAlgorithm
≪abstract≫ run() : void
node
1
Spec.
Link
state : LinkState
weight : EDouble
out
in
0..*
0..*
src
trg
1
1
≪enumeration≫ LinkState
Active : LinkState
Inactive : LinkState
Unclassified : LinkState
≪derived≫ allLinks
0..*
w(eab)
nb

## Slide 11: Topology Control Metamodel
Node
Link
state : LinkState
weight : EDouble
out
in
0..*
0..*
src
trg
1
1
≪enumeration≫ LinkState
Active : LinkState
Inactive : LinkState
Unclassified : LinkState
≪derived≫ allLinks
0..*
≪abstract≫
TopologyControlAlgorithm
≪abstract≫ run() : void
LStarKTCAlgorithm
k : EDouble
a : EDouble
run() : void
node
1
Spec.
User-defined attribute
hopCount : EInt
node
1
LMSTAlgorithm
run() : void
init() : void cleanup() : void
findShortestUnconnectedLink() : Link
TreeEntry
Tree
entry
0..1
entries
0..*
tree
1
0..1
parent
tree
1
entry
0..1
Custom methods
Auxiliary data structure
KTCAlgorithm
k : EDouble
run() : void
Custom algorithm parameters

## Slide 12: kTC story diagram
InactivateLinksInTriangles
KTCAlgorithm::run()
[Success]
[Failure]
[Failure]
max(maxWeight, e13.weight, e32.weight)
min(minWeight, e13.weight, e32.weight)
*(kMinWeight, minWeight, this.k)
>(e12.weight, maxWeight)
>(e12.weight, kMinWeight)
[Success]
ActivateRemainingLinks
e12: Link
state == UNCLASSIFIED
state := INACTIVE
this : LStarKTCAlgorithm
n2: Node
n3: Node
e13: Link
n1 : Node
e32 : Link
e12: Link
state == UNCLASSIFIED
state := ACTIVE
this : LStarKTCAlgorithm
n1 : Node
in
trg
trg
trg
src
src
src
out
out
in
node
out
in
src
out
node
Triangle pattern
Spec.
[FNT+98] Fischer et al.: "Story Diagrams: A New Graph Rewrite Language Based on the UML and Java," 1998
kTC: built-in constraints
while loops
while loops
Start
Stop

## Slide 13: Executing the kTC story diagram
n2 1
n3
1
2
2
2
3
6
n1
0
n4
1
After loop
"InactivateLinksInTriangle"
Spec.
n2 1
n3
1
2
2
2
3
6
n1
0
n4
1
e12: Link
state == UNCL.
state := INACTIVE
InactivateLinksInTriangles
LStarKTCAlgorithm::run()
[Failure]
[Failure]
this : LStarKTCAlgorithm
n2: Node
n3: Node
e13: Link
n1 : Node
e32 : Link
max(maxWeight, e13.weight, e32.weight)
min(minWeight, e13.weight, e32.weight)
*(kMinWeight, minWeight, this.k)
>(e12.weight, maxWeight)
>(e12.weight, kMinWeight)
e12: Link
state == UNCL.
state := ACTIVE
this : LStarKTCAlgorithm
n1 : Node
ActivateRemainingLinks
in
trg
trg
trg
src
src
src
out
out
in
node
out
in
src
out
node
[Success]
[Success]
After loop
"ActivateLinksInTriangle"
n2 1
n3
1
2
2
2
3
6
n1
0
n4
1
Initial
k=2
✘
n2 : Node
trg
in
match (only for type Node)
Legend

## Slide 14: l*-kTC story diagram
InactivateLinksInTriangles
LStarKTCAlgorithm::run()
[Success]
[Failure]
[Failure]
max(maxWeight, e13.weight, e32.weight)
min(minWeight, e13.weight, e32.weight)
*(kMinWeight, minWeight, this.k)
>(e12.weight, maxWeight)
>(e12.weight, kMinWeight)
hopCountOK(n1.hopCount, n2.hopCount, n3.hopCount, this.a)
[Success]
ActivateRemainingLinks
e12: Link
state == UNCLASSIFIED
state := INACTIVE
this : LStarKTCAlgorithm
n2: Node
n3: Node
e13: Link
n1 : Node
e32 : Link
e12: Link
state == UNCLASSIFIED
state := ACTIVE
this : LStarKTCAlgorithm
n1 : Node
in
trg
trg
trg
src
src
src
out
out
in
node
out
in
src
out
node
Spec.
[FNT+98] Fischer et al.: "Story Diagrams: A New Graph Rewrite Language Based on the UML and Java," 1998
l*-kTC: Custom constraint

## Slide 15: Code Generation for Testbed Evaluation
(i) Specification
(ii) Simulation
(iii) Testbed

## Slide 16: Contiki and ToCoCo as target platform
Contiki OS: widely used in the WSN community
ToCoCo – Topology Control framework for Contiki: rapid prototyping and evaluation of Topology Control algorithms
cMoflon creates a per subclass of
ToCoCo
Routing
TC
Topology abstraction
Power control
Radio module
Application
Neighbor discovery
Contiki
[Stein16] Stein et al.: "Control in Wireless Sensor Networks: What Blocks the Breakthrough?," In: LCN 2016
Source code on GitHub: https://github.com/steinmic/ToCoCo
Codegen.
TC
≪abstract≫
TopologyControlAlgorithm
≪abstract≫ run() : void

## Slide 17: A lean variant of eMoflon
Extensive reuse: Modeling frontend, preprocessing
Exchanged code generation phase (ca. 3400 LOC, 1% of eMoflon)
</>
.xmi
Metamodel
with story diagrams
Metamodel with
control flow models
EA export file
Standalone
EMF code
.java
Parser
M2M
Story diagrams
Attached to the corr. operations
User-defined code
ToCoCo
TC components
.c,.h
Common to
eMoflon & cMoflon
cMoflon
only
eMoflon only
I: Import
II: Validation
M2T
III: Code generation
TC
.ecore
Control flow models
User-defined attribute constraints
1:1 relation
Export of eMoflon
EA add-in
cMoflon
eMoflon
Codegen.
Notes: The reused parts of eMoflon consist of ca. 358 000 lines of Java
and C# code. In contrast, cMoflon consists of 3 362 lines of Java code (ca. 1%
of eMoflon).

## Slide 18: Example: Control flow code
Memory management (I):
free after use
Auxiliary type: Developer provides mapping (i.e., C struct)
Codegen.
InactivateLinksInTriangles
LStarKTCAlgorithm::run()
[Failure]
[Failure]
ActivateRemainingLinks
[Success]
[Success]
e12: Link
state == UNCL.
state := INACTIVE
InactivateLinksInTriangles
LStarKTCAlgorithm::run()
[Failure]
[Failure]
this : LStarKTCAlgorithm
n2: Node
n3: Node
e13: Link
n1 : Node
e32 : Link
max(maxWeight, e13.weight, e32.weight)
min(minWeight, e13.weight, e32.weight)
*(kMinWeight, minWeight, this.k)
>(e12.weight, maxWeight); >(e12.weight, kMinWeight)
hopCountOK(e12.hopCount, e13.hopCount, e32.hopCount, a)
e12: Link
state == UNCLASSIFIED
state := ACTIVE
this : LStarKTCAlgorithm
n1 : Node
ActivateRemainingLinks
in
trg
trg
trg
src
src
src
out
out
in
node
out
in
src
out
node
[Success]
[Success]
…
…
Traceability via story node names
Generic match representation: Array of void*
Story pattern decomposed into sub-patterns, e.g., for the LHS and RHS

## Slide 19: Example: Pattern matching code (I)
Codegen.
…
e12: Link
state == UNCL.
state := INACTIVE
this : LStarKTCAlgorithm
n2: Node
n3: Node
e13: Link
n1 : Node
e32 : Link
in
trg
trg
trg
src
src
src
out
out
in
node
out
in
this : LStarKTCAlgorithm
n1 : Node
e13: Link
Proper NULL pointer handling
n3: Node
Mimic object orientation by conventional names
…
e12: Link
state == UNCL.
state := INACTIVE
n2: Node
max(maxWeight, e13.weight, e32.weight)
min(minWeight, e13.weight, e32.weight)
*(kMinWeight, minWeight, this.k)
>(e12.weight, maxWeight); >(e12.weight, kMinWeight)
hopCountOK(e12.hopCount, e13.hopCount, e32.hopCount, a)
e32 : Link
User-defined l*-kTC
constraint

## Slide 20: Example: Pattern matching code (II)
Codegen.
…
e12: Link
state == UNCL.
state := INACTIVE
this : LStarKTCAlgorithm
n2: Node
n3: Node
e13: Link
n1 : Node
e32 : Link
in
trg
trg
trg
src
src
src
out
out
in
node
out
in
max(maxWeight, e13.weight, e32.weight)
min(minWeight, e13.weight, e32.weight)
*(kMinWeight, minWeight, this.k)
>(e12.weight, maxWeight); >(e12.weight, kMinWeight)
hopCountOK(e12.hopCount, e13.hopCount, e32.hopCount, a)
max(maxWeight, e13.weight, e32.weight)
min(minWeight, e13.weight, e32.weight)
*(kMinWeight, minWeight, this.k)
>(e12.weight, maxWeight); >(e12.weight, kMinWeight)
hopCountOK(e12.hopCount, e13.hopCount, e32.hopCount, a)
Memory mgmt. (II)
malloc on match, notification on error

## Slide 21: Evaluation for code size
… instead of runtime/scalability because (code) memory is scarcer (ca. 48kB)!
Size of compiled sensor images (Contiki 3.0), supp. resources available at https://github.com/eMoflon/cmoflon/releases/tag/cmoflon_1.0.0
Codegen.
Algorithm | Image Size[B] | Δ rel. to NoTC | Δ rel. to Man.
No TC | 36 917 |  | 
kTC Man Gen | 39 135 40 897 | +2 218 (+ 6.0 %) +3 980 (+10.8%) | +1 762 (+ 79.2%)
l*-kTC Man Gen | 40 293 42 247 | +3 376 (+ 9.1%) +5 330 (+14.4%) | +1 954 (+ 57.9%)
LMST Man Gen | 39 395 42 799 | +2 478 (+ 6.7%) +5 882 (+15.9%) | +3 404 (+137.4%)
Increase relative to image size: +4.8pp..+9.2pp
"Boilerplate:" OS + sample application
Notes: … instead of runtime/scalability because (code) memory is scarcer!
"Boilerplate" >37kB = 77% of 48kB
Size Increase:
  Relative to TC: +80% to 140% (no sophisticated code minimization!)
  Relative to whole image: +4.8% to 9.2%

## Slide 22: Summary and Outlook
Generate embedded C code of Topology Control algorithms
Extensible, dynamic memory & null-pointer handling
Compatible with previous simulation support
Outlook
More sensor platforms and algorithms
Improve memory allocation behavior
Reduce redundant null-pointer checks
Open source: eMoflon/cmoflon
(i) Specification: Story-driven modeling
(ii) Simulation:
Java
(iii) Testbed
eMoflon
(i) Specification: Story-driven modeling
(iii) Testbed: Embedded C
(ii) Simulation
cMoflon
+
</>
</>
Thank you!

## Slide 23: Thank You for Your Attention
Department of Electrical Engineering
and Information Technology
Real-Time Systems Lab
Roland Kluge, M.Sc.
roland.kluge@es.tu-darmstadt.de Phone: +49(0)6151 16-22354
Merckstraße 25 Fax: +49(0)6151 16-22352
64282 Darmstadt www.es.tu-darmstadt.de
Germany

## Slide 24: Icon sources
eMoflon/cMoflon logos: Work of the eMoflon developer team. Subject to Fair Use conditions.
TelosB Sensor node: Wiki Commons, CC-BY-3.0, by Jbasic, https://commons.wikimedia.org/wiki/File:TelosB.jpg
PowWow Sensor node: Wiki Commons, CC-BY-3.0, by Romain Fontaine, https://commons.wikimedia.org/wiki/File:PowWow.jpg
Writing Hand: CC-BY-3.0 US, Rediffusion, https://thenounproject.com/search/?q=hand%20drawing&i=29383
Gears: CC-BY-3.0 US, Pedro Santos https://thenounproject.com/search/?q=gear&i=1030299
Barrier: CC-BY-3.0 US, ProSymbols US, https://thenounproject.com/search/?q=barrier&i=792199
Lock: CC-BY-3.0 US, Aleksandr Vector, https://thenounproject.com/search/?q=lock&i=1009759
Light Bulb: CC-BY-3.0 US, ProSymbols, https://thenounproject.com/search/?q=idea%20bulb%20icon&i=799621
Target: CC-BY-3.0 US, Gregor Cresnar, https://thenounproject.com/search/?q=target&i=796213
GitHub Logo: CC-BY-3.0, Dave Gandy, http://www.flaticon.com/free-icon/github-logo_25231
These slides are provided under Creative Commons (BY-SA-NC-ND 3.0 EN)